## Slide 1: On Mixed-Criticality Scheduling: State of the Art
Haohan Li
Febrary 8, 2012
This presentation contains unpublished results.
Please do not distribute without permission.

## Slide 2: Models and Definitions
Task models
  By the way of generating jobs
    Independent jobs
    Sporadic task systems
      With arbitrary deadlines
      With implicit deadlines
  By the way of running on processor(s)
    Uniprocessor
    Multiprocessor
      Global scheduling
      Partitioned scheduling

## Slide 3: Models and Definitions
Definitions
  Mixed-criticality
    All level-X deadlines are met if no execution exceeds level-(X+1) WCET
  Speed-up factor
    Factor that a processor needs to speed up to schedule all non-over-utilized systems

## Slide 4: Models and Definitions
Scheduling algorithms
  By priority alternations
    FTP: Fixed-Task-Priority
    FJP: Fixed-Job-Priority
    DP: Dynamic-Priority
  By clairvoyance
    Clairvoyant scheduling: Knowing all jobs’ execution times before actual run
    On-line scheduling: Jobs’ execution times only revealed when executed

## Slide 5: State of the Art
Independent jobs
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    OCBP, 1.618,2.15,2.63…, -, X

## Slide 6: Baruah et al., IEEE-TC 2011
Scheduling real-time mixed-criticality jobs
  OCBP algorithm on mixed-criticality jobs
    OCBP: keep finding the job that can be the lowest-priority job; use Ci(LO) for LO-jobs and Ci(HI) for HI-jobs
  Speed-up factor result on arbitrary criticality levels
    xL=(1+x)L-1
  Proved to be optimal with respect to speed-up factor, for on-line scheduling algorithms

## Slide 7: State of the Art
Independent jobs
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    OCBP, 1.618,2.15,2.63…, -, X
    CBEDF, 1.618, -, 2

## Slide 8: Park & Kim, EMSOFT 2011
Dynamic Scheduling Algorithm and Its Schedulability Analysis for Certifiable Dual-Criticality Systems
  Declaring the domination of CBEDF (Criticality Based Earliest Deadline First) over OCBP, on independent jobs

## Slide 9: State of the Art
Independent jobs
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    OCBP, 1.618,2.15,2.63…, -, X
    CBEDF, 1.618, -, 2
    TT, 1.618, -, 2

## Slide 10: Baruah & Fohler, RTSS 2011
Certification-cognizant time-triggered scheduling of mixed-criticality systems
  TT: Time-Triggered
  Building a scheduling table for independent jobs
  With speed-up factor 1.618

## Slide 11: State of the Art
Independent jobs
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    OCBP, 1.618,2.15,2.63…, -, X
    CBEDF, 1.618, -, 2
    TT, 1.618, -, 2
  Multiprocessor
    OCBP, 2.618-1/m, -, 2

## Slide 12: Baruah et al., ESA 2011
Mixed-Criticality Scheduling of Sporadic Task Systems
  In the last section of this paper, the authors shortly introduced an extension of OCBP to multiprocessors
    The speed-up factor is 1.618+1-1/m

## Slide 13: State of the Art
Method/ Speed-up factor/ Run-time complexity/ Criticality level # | Uniprocessor | Multiprocessor: Global | Multiprocessor: Partitioned
Independent jobs | OCBP/1.618,2.15,2.63…/-/X, CBEDF/1.618/-/2, TT/1.618/-/2 | OCBP/2.618-1/m/-/2 | 
Sporadic task system with arbitrary-deadlines |  |  | 
Sporadic task system with implicit-deadlines |  |  | 

## Slide 14: State of the Art
Sporadic task system with arbitrary-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    PLRS, 1.618,2.15,2.63…, O(N2), X

## Slide 15: Guan et al., RTSS 2011
Effective and Efficient Scheduling of Certifiable Mixed-Criticality Sporadic Task Systems
  PLRS (Priority List Reuse Scheduling) is claimed to dominate OCBP
  The speed-up factor is the same as OCBP
  The run-time complexity is O(N2), where N is the number of tasks

## Slide 16: State of the Art
Sporadic task system with arbitrary-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    PLRS, 1.618,2.15,2.63…, O(N2), X
    EDF-VD, 1.89, O(log N), 2 ---- unpublished
    AMC, 2,3,4…, O(log N), X
      Respectively DP, FJP, FTP

## Slide 17: Baruah, Burns & Davis, RTSS 2011
Response-Time Analysis for Mixed Criticality Systems
  AMC (Adaptive Mixed Criticality): A fixed-priority scheduling algorithm

## Slide 18: Dorin et al., Real-Time Syst 2010
Schedulability and sensitivity analysis of multiple criticality tasks with fixed-priorities
  This paper shows the optimal speed-up factor of fixed-priority algorithms on X criticality levels is X

## Slide 19: State of the Art
Sporadic task system with arbitrary-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    PLRS, 1.618,2.15,2.63…, O(N2), X
    EDF-VD, 1.89, O(log N), 2 ---- unpublished
    AMC, 2,3,4…, O(log N), X
      Respectively DP, FJP, FTP
  Multiprocessor: Global
  Multiprocessor: Partitioned
    On going by Guan et al., on RTAS 2012?

## Slide 20: State of the Art
Method/ Speed-up factor/ Run-time complexity/ Criticality level # | Uniprocessor | Multiprocessor: Global | Multiprocessor: Partitioned
Independent jobs | OCBP/1.618,2.15,2.63…/-/X, CBEDF/1.618/-/2, TT/1.618/-/2 | OCBP/2.618-1/m/-/2 | 
Sporadic task system with arbitrary-deadlines | PLRS/1.618,2.15,2.63…/O(N2)/X, EDF-VD/1.89/O(log N)/2, AMC/2,3,4…/O(log N)/X | - | On going?
Sporadic task system with implicit-deadlines |  |  | 

## Slide 21: State of the Art
Sporadic task system with implicit-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    EDF-VD/1.618,2.07,2.57…/O(log N)/X

## Slide 22: Baruah et al, ESA 2011
Mixed-Criticality Scheduling of Sporadic Task Systems
  EDF-VD (Virtual Deadlines): Giving the HI jobs a shorter deadline before criticality change, and using EDF scheduler
  Speed-up factors are respectively 1.618,2.07,2.57…, no closed formula
    OCBP is 1.618, 2.15, 2.63…, for your comparison
  It handles arbitrary criticalities but isn’t proved optimal

## Slide 23: State of the Art
Sporadic task system with implicit-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    EDF-VD/1.618,2.07,2.57…/O(log N)/X
      EDF-VD/1.33/O(log N)/2

## Slide 24: Baruah et al., ECRTS 2011 submission
The preemptive uniprocessor scheduling of mixed-criticality implicit-deadline sporadic task systems
  Still using EDF-VD, but giving a better speed-up factor 1.33 for two-criticality situation
  Proved to be optimal with respect to speed-up factor on implicit-deadline systems
    Why it can be smaller than 1.618, which is the optimal factor of independent jobs?

## Slide 25: State of the Art
Sporadic task system with implicit-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    EDF-VD/1.618,2.07,2.57…/O(log N)/X
      EDF-VD/1.33/O(log N)/2
  Multiprocessor: Global
    GEDF-VD/3.236/O(log N)/2

## Slide 26: Li & Baruah, ECRTS 2011 submission
Global mixed-criticality scheduling on multiprocessors
  GEDF-VD: Basically GEDF + EDF-VD
  The speed-up factor is 2x1.618 = 3.236

## Slide 27: State of the Art
Sporadic task system with implicit-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    EDF-VD/1.618,2.07,2.57…/O(log N)/X
      EDF-VD/1.33/O(log N)/2
  Multiprocessor: Global
    GEDF-VD/3.236/O(log N)/2
  Multiprocessor: Partitioned
    EDF-VD/1.618+ε,2.07+ ε,2.57+ ε…/O(log N)/X

## Slide 28: Baruah et al, ESA 2011
Mixed-Criticality Scheduling of Sporadic Task Systems
  Partitioning the tasks by reducing them to two-dimensional vector scheduling problem, then using EDF-VD on each processor
    There is a PTAS (polynomial-time approximation scheme) for the problem, which means there is a P-algorithm for every given constant ε

## Slide 29: State of the Art
Sporadic task system with implicit-deadlines
      Method/Speed-up factor/Run-time complexity/Criticality level #
  Uniprocessor
    EDF-VD/1.618,2.07,2.57…/O(log N)/X
      EDF-VD/1.33/O(log N)/2
  Multiprocessor: Global
    GEDF-VD/3.236/O(log N)/2
  Multiprocessor: Partitioned
    EDF-VD/1.618+ε,2.07+ ε,2.57+ ε…/O(log N)/X
      Partitioning using our 1.33 factor is on-going

## Slide 30: State of the Art
Method/ Speed-up factor/ Run-time complexity/ Criticality level # | Uniprocessor | Multiprocessor: Global | Multiprocessor: Partitioned
Independent jobs | OCBP/1.618,2.15,2.63…/-/X, CBEDF/1.618/-/2, TT/1.618/-/2 | OCBP/2.618-1/m/-/2 | 
Sporadic task system with arbitrary-deadlines | PLRS/1.618,2.15,2.63…/O(N2)/X, EDF-VD/1.89/O(log N)/2, AMC/2,3,4…/O(log N)/X | - | On going?
Sporadic task system with implicit-deadlines | EDF-VD/1.618,2.07,2.57… /O(log N)/X EDF-VD/1.33/O(log N)/2 | GEDF-VD/3.236/O(log N)/2 | EDF-VD/ 1.618+ε,2.07+ ε,2.57+ ε…/ O(log N)/X

## Slide 31: Open Problems
Method/ Speed-up factor/ Run-time complexity/ Criticality level # | Uniprocessor | Multiprocessor: Global | Multiprocessor: Partitioned
Independent jobs | OCBP/1.618,2.15,2.63…/-/X, CBEDF/1.618/-/2, TT/1.618/-/2 | OCBP/2.618-1/m/-/2 | 
Sporadic task system with arbitrary-deadlines | PLRS/1.618,2.15,2.63…/O(N2)/X, EDF-VD/1.89/O(log N)/2, AMC/2,3,4…/O(log N)/X | - | On going?
Sporadic task system with implicit-deadlines | EDF-VD/1.618,2.07,2.57… /O(log N)/X EDF-VD/1.33/O(log N)/2 | GEDF-VD/3.236/O(log N)/2 | EDF-VD/ 1.618+ε,2.07+ ε,2.57+ ε…/ O(log N)/X